## Slide 1: progress report Visual Noise Reduction
By: Matt Kramer, Evan Wilder, Evan Kwok
Notes: Remind about the project

## Slide 2: Scope Changes
Project will focus mainly on attenuation of unwanted visual stimuli
  In order to:
    Create a more robust system
    Maintain timeline of the class
Need Statement remains unchanged
Attenuation
Detection
Design
Notes: Highest likelihood of success with the project comes with maximizing for one variable

## Slide 3: Design Specs Changes
Dynamic response
Ease of troubleshooting
Ease of setup
Accuracy in defining region of interest(ROI)
No Schedule or team responsibility changes
Removed Specs
Added Specs
Responsiveness to changes in region of interest

## Slide 4: Design alternatives

## Slide 5: Self made Augmented reality(AR)
Main Features: Plastic Visor, Phone App
  Visor: 4 laser cut pieces of plastic
  App: Software development
Phone projects image into the field of view
  black light would be projected around the region of interest(ROI)
  This projection attenuates the visual noise

## Slide 6: Commercial aR
Similar idea for attenuation as the homemade AR system
  Placement of black light in visual field
  Improvement on attenuation
Improves on fundamental issues of a homemade AR
  BUT at what cost??
Appeal: systems typically have software developer kits (SDK)
  Large communities of platform developers
Full Virtual Reality is even further out of the price range so I will move on

## Slide 7: Manual Blocking: shields
First of two solutions that physically blocks the user’s visual
Adds on to an eye glass form
Involves 4 opaque “shields” per lens
  Slide in pairs, top/bottom and right/left
  Either manual movement or servo
Left and right lens will be synchronized
User adjustment of the visual field
Rectangular field of view

## Slide 8: Manual Blocking: Aperture
Second manual blocking solution
Frame will be 3D printed and parted with an aperture mechanism
Similar to a camera aperture
Rotation in one direction narrows the ROI and an opposite turn widens the ROI
Overlapping blades attenuates outside the user’s ROI
Circular field of view

## Slide 9: Polymer dispersed light crystal(PDLC) glass with accelerometer
PDLC is two thin layers of glass with an opaque polymer in between
  Without a potential, PDLC is opaque
  With a potential, PDLC is clear
Off glasses form
PDLC layers glass lenses with circular hole
Pairing PDLC with an accelerometer
  Holding head still blocks outside a predefined, circular ROI
  Moving head, allows for full visual field
Circular field of view

## Slide 10: Pugh Analysis
Design requirement | Weight | Homemade AR | Commercial AR | Commercial VR | Smart glass with accelerometer | Manual blocking “shields” | Manual blocking aperture
Safety for the user | 10 | 10 | 10 | 6 | 10 | 7 | 7
Comfort | 7 | 5 | 8 | 7 | 6 | 6 | 6
Ease of use/ practicality | 7 | 6 | 7 | 3 | 7 | 4 | 5
Effectively attenuates areas outside ROI | 8 | 3 | 6 | 10 | 9 | 10 | 10
Clarity of the ROI | 9 | 10 | 10 | 6 | 10 | 10 | 10
Compatibility with other devices | 7 | 6 | 5 | 4 | 10 | 10 | 10
Compatibility with workspace | 6 | 10 | 10 | 5 | 10 | 10 | 10
Responsiveness to Changes in ROI | 8 | 9 | 9 | 2 | 9 | 3 | 2
Portability | 6 | 8 | 7 | 2 | 10 | 10 | 10
Cost | 8 | 10 | 2 | 1 | 6 | 10 | 10
Battery life | 7 | 6 | 8 | 4 | 10 | 10 | 10
Device weight | 4 | 5 | 7 | 2 | 7 | 7 | 10
Total | 87 | 655 | 652 | 394 | 761 | 702 | 713
Normalized Average Rating |  | 7.5287356 | 7.49425 | 4.52874 | 8.74713 | 8.06897 | 8.1954
Design requirement | Weight | Homemade AR | Commercial AR | Commercial VR | Smart glass with accelerometer | Manual blocking “shields” | Manual blocking aperture
Safety for the user | 10 | 10 | 10 | 6 | 10 | 7 | 7
Comfort | 7 | 5 | 8 | 7 | 6 | 6 | 6
Ease of use/ practicality | 7 | 6 | 7 | 3 | 7 | 4 | 5
Effectively attenuates areas outside ROI | 8 | 3 | 6 | 10 | 9 | 10 | 10
Clarity of the ROI | 9 | 10 | 10 | 6 | 10 | 10 | 10
Compatibility with other devices | 7 | 6 | 5 | 4 | 10 | 10 | 10
Compatibility with workspace | 6 | 10 | 10 | 5 | 10 | 10 | 10
Responsiveness to Changes in ROI | 8 | 9 | 9 | 2 | 9 | 3 | 2
Portability | 6 | 8 | 7 | 2 | 10 | 10 | 10
Cost | 8 | 10 | 2 | 1 | 6 | 10 | 10
Battery life | 7 | 6 | 8 | 4 | 10 | 10 | 10
Device weight | 4 | 5 | 7 | 2 | 7 | 7 | 10
Total |  | 655 | 652 | 394 | 761 | 702 | 713

## Slide 11: Pugh Analysis
Design requirement | Weight | Homemade AR | Commercial AR | Commercial VR | Smart glass with accelerometer | Manual blocking “shields” | Manual blocking aperture
Safety for the user | 10 | 10 | 10 | 6 | 10 | 7 | 7
Comfort | 7 | 5 | 8 | 7 | 6 | 6 | 6
Ease of use/ practicality | 7 | 6 | 7 | 3 | 7 | 4 | 5
Effectively attenuates areas outside ROI | 8 | 3 | 6 | 10 | 9 | 10 | 10
Clarity of the ROI | 9 | 10 | 10 | 6 | 10 | 10 | 10
Compatibility with other devices | 7 | 6 | 5 | 4 | 10 | 10 | 10
Compatibility with workspace | 6 | 10 | 10 | 5 | 10 | 10 | 10
Responsiveness to Changes in ROI | 8 | 9 | 9 | 2 | 9 | 3 | 2
Portability | 6 | 8 | 7 | 2 | 10 | 10 | 10
Cost | 8 | 10 | 2 | 1 | 6 | 10 | 10
Battery life | 7 | 6 | 8 | 4 | 10 | 10 | 10
Device weight | 4 | 5 | 7 | 2 | 7 | 7 | 10
Total | 87 | 655 | 652 | 394 | 761 | 702 | 713
Normalized Average Rating |  | 7.5287356 | 7.49425 | 4.52874 | 8.74713 | 8.06897 | 8.1954
Design requirement | Weight | Homemade AR | Commercial AR | Commercial VR | Smart glass with accelerometer | Manual blocking “shields” | Manual blocking aperture
Safety for the user | 10 | 10 | 10 | 6 | 10 | 7 | 7
Comfort | 7 | 5 | 8 | 7 | 6 | 6 | 6
Ease of use/ practicality | 7 | 6 | 7 | 3 | 7 | 4 | 5
Effectively attenuates areas outside ROI | 8 | 3 | 6 | 10 | 9 | 10 | 10
Clarity of the ROI | 9 | 10 | 10 | 6 | 10 | 10 | 10
Compatibility with other devices | 7 | 6 | 5 | 4 | 10 | 10 | 10
Compatibility with workspace | 6 | 10 | 10 | 5 | 10 | 10 | 10
Responsiveness to Changes in ROI | 8 | 9 | 9 | 2 | 9 | 3 | 2
Portability | 6 | 8 | 7 | 2 | 10 | 10 | 10
Cost | 8 | 10 | 2 | 1 | 6 | 10 | 10
Battery life | 7 | 6 | 8 | 4 | 10 | 10 | 10
Device weight | 4 | 5 | 7 | 2 | 7 | 7 | 10
Total |  | 655 | 652 | 394 | 761 | 702 | 713

## Slide 12: Pugh Analysis
Design requirement | Weight | Homemade AR | Commercial AR | Commercial VR | Smart glass with accelerometer | Manual blocking “shields” | Manual blocking aperture
Safety for the user | 10 | 10 | 10 | 6 | 10 | 7 | 7
Comfort | 7 | 5 | 8 | 7 | 6 | 6 | 6
Ease of use/ practicality | 7 | 6 | 7 | 3 | 7 | 4 | 5
Effectively attenuates areas outside ROI | 8 | 3 | 6 | 10 | 9 | 10 | 10
Clarity of the ROI | 9 | 10 | 10 | 6 | 10 | 10 | 10
Compatibility with other devices | 7 | 6 | 5 | 4 | 10 | 10 | 10
Compatibility with workspace | 6 | 10 | 10 | 5 | 10 | 10 | 10
Responsiveness to Changes in ROI | 8 | 9 | 9 | 2 | 9 | 3 | 2
Portability | 6 | 8 | 7 | 2 | 10 | 10 | 10
Cost | 8 | 10 | 2 | 1 | 6 | 10 | 10
Battery life | 7 | 6 | 8 | 4 | 10 | 10 | 10
Device weight | 4 | 5 | 7 | 2 | 7 | 7 | 10
Total | 87 | 655 | 652 | 394 | 761 | 702 | 713
Normalized Average Rating |  | 7.5287356 | 7.49425 | 4.52874 | 8.74713 | 8.06897 | 8.1954
Design requirement | Weight | Homemade AR | Commercial AR | Commercial VR | Smart glass with accelerometer | Manual blocking “shields” | Manual blocking aperture
Safety for the user | 10 | 10 | 10 | 6 | 10 | 7 | 7
Comfort | 7 | 5 | 8 | 7 | 6 | 6 | 6
Ease of use/ practicality | 7 | 6 | 7 | 3 | 7 | 4 | 5
Effectively attenuates areas outside ROI | 8 | 3 | 6 | 10 | 9 | 10 | 10
Clarity of the ROI | 9 | 10 | 10 | 6 | 10 | 10 | 10
Compatibility with other devices | 7 | 6 | 5 | 4 | 10 | 10 | 10
Compatibility with workspace | 6 | 10 | 10 | 5 | 10 | 10 | 10
Responsiveness to Changes in ROI | 8 | 9 | 9 | 2 | 9 | 3 | 2
Portability | 6 | 8 | 7 | 2 | 10 | 10 | 10
Cost | 8 | 10 | 2 | 1 | 6 | 10 | 10
Battery life | 7 | 6 | 8 | 4 | 10 | 10 | 10
Device weight | 4 | 5 | 7 | 2 | 7 | 7 | 10
Total |  | 655 | 652 | 394 | 761 | 702 | 713
Notes: Mention weights – project is all about RIO

## Slide 13: Chosen solution:

## Slide 14: Chosen solution:
PDLC with Accelerometer
Notes: Reminder of PDLC

## Slide 15: More on PDLC with accelerometer
3D lens/frames with some resemblance to safety goggles
Accelerometer mounted closer to lenses
PDLC film will layer the lenses, with circle cut out of the center
Microcontroller connects the accelerometer to the PDLC film
Power will be supplied to the microcontroller
A large movement will apply voltage to PDLC
PDLC film
Accelero-
meter
Lens
Micro-Controller
Notes: Reminder of PDLC film

## Slide 16: More on using the solution
“Movements” result in clearing visual field
  Definition of a movement is not defined
  Will use accelerometer data as input
Lack of movement attenuates outside the ROI
Typically PDLC used as “on” or “off”
  Can vary the opaqueness with a changing potential

## Slide 17: Budget
PDLC Film $200
Microcontroller $50-100
Batteries $50-100
3D printed filament $20
Accelerometer $20
Unexpected Expenses (Shipping, Wiring, $200
Replacement, Parts, etc.)
Total $640

## Slide 18: Questions?